## 2D flow around an oscillating cylinder - $Re_{H}= 185$
Numerical study based on the publication of Pham et al., Journal of Marine Science and Technology, Vol. 18, No. 3, pp. 361-368 (2010) The motion of the cylinder is vertical and forced with a sinusoïdal function

Author : Y. Fraigneau, LISN, UMR CNRS 9015 (yann.fraigneau@lisn.fr)
Date : July 2016
Simulation type : DNS (code Sunfluidh – Sunfluidh code)
Location : /DATABASE_2DFLOW_AROUND_OSCILLATING_CYLINDER_DNS
Status : Free access for laboratory members, on request for external members
Data size : ~ 7 Gb

A video is available here
Come back to first page

### Simulation settings

#### 2D sketch

#### Referential : cartesian geometry
1. axes :
  1. x(i) : downstream direction
  2. y(j) : normal direction
2. origin :
  1. : centre of the cylinder
  2. : mid-height
#### Reference scales
- Density : mass density of the fluid ()
- Length : cylinder diameter ()
- Velocity : velocity at inlet ()
- Dynamic viscosity : dynamic viscosity of the fluid ()
- Reynolds number :
- Strouhal number : (oscillating-cylinder frequency over vortex-shedding frequency when the cylinder is at rest)
- motion magnitude : (where A is the motion factor)
#### Non-dimensionalised data
- velocity :
- density :
- coordinates : ,
#### Computational domain
1. Domain scope
  1. computational domain size
    1. Downstream direction(x) : (upward part , downward part )
    2. Normal direction (y) :
  2. Oscillating cylinder (vertical oscillating motion around the mid-height of the domain)
    1. centre position at rest : and
    2. diameter:
    3. oscillation frequency : or
    4. The cylinder is modeled with a pseudo-penalisation method (Pasquetti et al., Applied Numerical Mathematics, 2008)
2. Boundary conditions
  1. Inlet : imposed pressure uniform velocity ()
  2. Outlet : Orlansky type
  3. Bottom and top conditions : symmetry
3. Spatial resolution
  1. mesh size : (576.000 cells)
  2. About cell-size
    1. : from to (downstream direction)
    2. : from to (normal direction)
Come back to first page

### Data features

- Time series
  - from probes
    - Physical quantities : velocity components along x and y directions (u,v) and pressure (p)
    - 1 probe
    - Time step= time unit
    - Time range : 400 to 600 time units
    - Location : Xi= 3.5 , Xj=0.0
    - File name (per physical quantity): x_ins_00000.d with x= u,v,p
  - about cylinder motion
    - center position as a function of time (ASCII file ibm_position01.dat)
    - cylinder velocity as a function of time (ASCII file ibm_velocity01.dat)
    - global force components applied to the cylinder (ASCII file ibm_force01.dat)
    - force contributions exerted on the moving cylinder (ASCII file ibm_force_contribution01.dat, the four last columns can be ignored)
- 3D snapshots
  - Instantaneous fields : velocity components in x, y and z directions (U,V), the pressure (P) and the phase function related to the body motion (TRACE)
  - Recording rate : 0.4 time unit
  - Time range from from 200.0 to 600.0 time units
  - File name : res_xxxxx_yyyyyyy.d
    - MPI subdomain ID: 0
    - Time ID : from 3 to 502
Come back to first page

### Database organisation

Data size : ~ 7 Gb
Main directory : /vol/DATABASE_MECA/DATABASE_2DFLOW_AROUND_OSCILLATING_CYLINDER_DNS
For more details about files, see the wiki doc of Sunfluidh
Intermediate directories (four cases of study)
- and - directory : CAS_F0.95_A0.2
- and - directory : CAS_F0.95_A0.5
- and - directory : CAS_F1.2_A0.2
- and - directory : CAS_F1.2_A0.5
Endpoint directories & files

  /DATASETUP : ASCII files
        input data file for sunfluidh : input3d.dat
  /GRID : ASCII files
        input data file : data_meshgen.d
        grid files for sunfluidh: maillx.d, mailly.d, maillz.d
  /SNAPSHOTS : snapshots binary files res_xxxxx_yyyyyyy.d
  /TIMESERIES : ASCII files
        u_ins_00000.d , v_ins_00000.d and p_ins_00000.d (timeseries of the velocity components and pressure from probe)
        ibm_position01.dat, ibm_velocity01.dat (about cylinder motion)
        ibm_force01.dat, ibm_force_contribution01.dat (about forces exerted on the cylinder)
Come back to first page