## 3D shear-layer driven cavity flow with forcing term at $Re_{L_c}= 7826$
Author : Y. Fraigneau CNRS-LIMSI (yann.fraigneau@limsi.fr)
Date : July 2020
Simulation type : DNS (Sunfluidh code)
Location : DATABASE_CAVITY3D_R2_RE7826_PER1.0_DNS/FORCINGTERM
Status : Free access
Data size : ~ 8.6 Gb

A video is available here
Come back to first page

### Simulation settings

#### 2D sketch

#### Referential : cartesian geometry
1. axes :
  1. x(i) : downstream direction
  2. y(j) : normal direction
  3. z(k) : spanwise direction
2. origin :
  1. : upstream edge of the cavity
  2. : upstream edge of the cavity
  3. : upstream edge of the cavity, at the mid-span location
#### Reference scales
- Density : mass density of the fluid ()
- Length : cavity length ()
- Velocity : inlet bulk velocity ()
- Dynamic viscosity : dynamic viscosity of the fluid ()
- Reynolds number :
#### Non-dimensionalised data
- velocity :
- density :
- coordinates : , ,
#### Computational domain
1. Domain scope
  1. Downstream direction(x) :
  2. Normal direction (y) :
  3. Spanwise direction (z) :
  4. upstream vein length :
  5. cavity height :
2. Boundary conditions
  1. Inlet : Blasius' profile at . Boundary layer thickness
  2. Outlet : Orlansky's type at
  3. Wall conditions : floor and cavity walls
  4. Periodicity : lateral ends of the domain (spanwise direction)
  5. Symmetry plan : top of the domain
3. Spatial resolution
  1. Grid : per subdomain (1.572.864 cells over the domain)
  2. About cell-size
    1. (downstream direction)
    2. (normal direction)
    3. (spanwise direction)
#### Forcing term modeling
- Location : In front of the uptream edge of cavity
- Zone area : brick volume : , center located at : ()
- forcing term modeled with the pseudo-penalty approach (Pasquetti et al., Applied Numerical Mathematics 58 (2008))
  - force applied in the zone area defined as :
  - (the numerical time step)
Come back to first page

### Data features

- Time series from probes
  - Physical quantities : velocity components along x, y and z directions (u,v,w) and pressure (p)
  - 11 probes
  - Time step= 0.0525 time unit
  - Time range : 25.02 to 259.96 time units
  - Locations (In vertical mid-plan at )
    - Xi=0.2 , Xj= -0.3 , Xk= 0.0
    - Xi=0.5 , Xj= -0.3 , Xk= 0.0
    - Xi=0.8 , Xj= -0.3 , Xk= 0.0
    - Xi=0.1 , Xj= 0.05 , Xk= 0.0
    - Xi=0.5 , Xj= 0.05 , Xk= 0.0
    - Xi=0.9 , Xj= 0.05 , Xk= 0.0
    - Xi=1.0 , Xj= 0.05 , Xk= 0.0
  - File name (per physical quantity) : x_ins_yyyyy.d with x= u,v,w,p and 'yyyyy' the MPI subdomain ID
- 3D snapshots
  - Instantaneous fields : velocity components in x, y and z directions (U,V,W) and pressure (P)
  - Recording rate : 0.25 time unit
  - Time range from from 210.0 to 260.0 time units
  - File name : res_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID: 0
    - Time ID : from 39 to 239
- 2D slices
  - Instantaneous fields : velocity components in x, y and z directions (U,V,W) and pressure (P)
  - Recording rate : 0.05 time units
  - Time range from from 210 to 260 time units
  - File name : slice_n_idir_xxxxx_yyyyyyy.d (n : slice number ID, idir : normal orientation= 1: x(i), 2: y(j), 3: z(k), xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID: 0
    - Time ID : from 1 to 1001
  - 8 slices
    - slice ID : 1 - normal orientation : spanwise - location :
    - slice ID : 2 - normal orientation : spanwise - location :
    - slice ID : 3 - normal orientation : spanwise - location :
    - slice ID : 4 - normal orientation : spanwise - location :
    - slice ID : 5 - normal orientation : spanwise - location :
    - slice ID : 6 - normal orientation : spanwise - location :
    - slice ID : 7 - normal orientation : normal - location :
    - slice ID : 8 - normal orientation : normal - location :
- Statistics
  - fields : (i,j : indexes of direction x, y or z)
    - Mean fields of velocity components (<Ui>) and pressure (<P>)
    - Mean fields of quadratic quantities (<P2>, <UiUj>)
  - Time average computation
  - Time startup = 210.0 time units
  - Time range per file = 50.0 time units
  - Total time range from 180.0 to 510.0 time units
  - file name : rst_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID : 0
    - Time ID : 1
Come back to first page

### Database organisation

Data size : ~ 8.6 Gb
Main directory : /vol/DATABASE_MECA/DATABASE_CAVITY3D_R2_RE7826_PER1.0_DNS/FORCINGTERM
For more details about files, see the wiki doc of Sunfluidh
#### Directories & files
  /GRID : contains all ASCII files about grid setup
     input data file : data_meshgen.d
     report on grid features : report_meshgen.d
     grid files for sunfluidh: maillx.d, mailly.d, maillz.d
     check files (ASCII) : check_mesh_I.d,check_mesh_J.d,check_mesh_K.d
        (3 columns : indices, cell-face coordinates, cell size)
  /DATASETUP : ASCII files
   input data file for sunfluidh : input3d.dat
   velocity profile (Blasius' boundary layer) at the inlet : inlet_velocity_profile.dat
  /TIMESERIES : contains time series recorded over the time range [200,513.3]
        ASCII files : x_ins_00000_full.d with x= u,v,w,p
  /SNAPSHOTS : snapshots binary files res_xxxxx_yyyyyyy.d
  /STATISTICS : statistics binary files files rst_xxxxx_yyyyyyy.d
  /RESTART_AR : backup/restart archive save_t260.tar at 260.0 time units
Come back to first page