## 3D turbulent channel flow at $Re_{\tau}= 590$
Author : Y. Fraigneau CNRS-LIMSI (yann.fraigneau@limsi.fr)
Date : August 2020
Location : DATABASE_CHANNELFLOW_RETAU590_LES
Simulation type : LES, Mansour's model (Sunfluidh code)

Come back to previous page

### Simulation settings

#### Sketch

#### Referential : cartesian geometry
1. axes :
  1. x(i) : downstream direction
  2. y(j) : spanwise direction
  3. z(k) : normal direction
2. origin :
  1. : left down corner
  2. : left down corner
  3. : left down corner
#### Reference scales
- Density : mass density of the fluid ()
- Length : half height of the channel ()
- Velocity : wall friction velocity ()
- Dynamic viscosity : dynamic viscosity of the fluid ()
- Reynolds number :
#### Non-dimensionalised data
- velocity :
- density :
- coordinates : , ,
#### Computational domain
1. Domain scope
  1. Downstream direction(x) :
  2. Spanwise direction (y) :
  3. Normal direction (z) :
2. Boundary conditions
  1. Wall conditions : Top and low walls of the domain
  2. Periodicity : lateral ends of the domain in and directions
3. Domain decomposition (128 MPI subdomains)
  1. Along the downstream direction : 8
  2. Along the normal direction : 4
  3. Along the spanwise direction : 4
4. Spatial resolution :
  1. Grid : per subdomain (16.777.216 cells over the domain)
  2. About cell-size
    1. (downstream direction)
    2. (spanwise direction)
    3. (normal direction)

### Data Recording : information about data types

- Time series from probes
  - Physical quantities : velocity components along x,y and z directions (u,v,w) and pressure (p)
  - 9 probes
  - Time step= 0.001
  - Time range : 16.64 to 199.44 time units
  - Locations (In vertical plan at )
    - Xi= 1.00, Xj= 1.00 , Xk= 0.10 - MPI Subdomain ID : 20
    - Xi= 1.00, Xj= 1.00 , Xk= 0.25 - MPI Subdomain ID : 21
    - Xi= 1.00, Xj= 1.00 , Xk= 0.50 - MPI Subdomain ID : 21
    - Xi= 1.00, Xj= 1.00 , Xk= 0.75 - MPI Subdomain ID : 21
    - Xi= 1.00, Xj= 1.00 , Xk= 1.00 - MPI Subdomain ID : 21
    - Xi= 1.00, Xj= 1.00 , Xk= 1.25 - MPI Subdomain ID : 22
    - Xi= 1.00, Xj= 1.00 , Xk= 1.50 - MPI Subdomain ID : 22
    - Xi= 1.00, Xj= 1.00 , Xk= 1.75 - MPI Subdomain ID : 22
    - Xi= 1.00, Xj= 1.00 , Xk= 1.90 - MPI Subdomain ID : 23
File name : x_ins_yyyyy.d with x= u,v,w,p and 'yyyyy' the MPI subdomain ID
- 3D snapshots
  - Instantaneous fields : velocity components U,V,W and pressure (P)
  - Recording rate : 0.01 time units
  - Time range from from 16.64 to 199.44
  - File name : res_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID: from 0 to 127
    - Time ID : from 9 to 18288
- Statistics
  - fields : (i,j : indexes of direction x, y or z)
    - Mean fields of velocity components (<Ui>) and pressure (<P>)
    - Mean fields of square quantities (<P2>, <UiUj>)
    - Mean field of subgrid dynamic viscosity (mu_sg)
    - Mean field of square of subgrid dynamic viscosity (musg2)
  - Time average computation
  - Time startup = 20.0
  - Time range per file = 5.0
  - Total time range from 20.0 to 199.44
  - file name : rst_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID : from 0 to 127
    - Time ID : from 1 to 35

### Database organisation

Data size : ~ 5.1 To
Main directory : /vol/DATABASE_MECA/RESTRICTED_ACCESS/DATABASE_CHANNELFLOW_RETAU590_LES
For more details about files, see the the wiki doc of Sunfluidh
#### Directories & files
  /GRID : contains all ASCII files about grid setup
     input data file : data_meshgen.d
     report on grid features : report_meshgen.d
     grid files for sunfluidh: maillx.d, mailly.d, maillz.d
     check files (ASCII) : check_mesh_I.d,check_mesh_J.d,check_mesh_K.d
        (3 columns : indices, cell-face coordinates, cell size)
  /DATASETUP : ASCII files
   input data file for sunfluidh : input3d.dat
  /TIMESERIES : contains time series recorded over the time range [16.64 ; 199.44]
        ASCII files : x_ins_yyyyy.d with x= u,v,w,p
        time series files are sliced in storage directories CAS-MPI200-n (n from 5 to 50)
  /SNAPSHOTS : snapshots binary files res_xxxxx_yyyyyyy.d
        files stored in archive files : res_yyyyyyy.tar for each time ID
  /STATISTICS : statistics binary files files rst_xxxxx_yyyyyyy.d
        files stored in archive files : res_z.tar , z is an ID number (from 1 to 35)
  /RESTART_AR : backup/restart archive save.tar at time 199.44
  /FROM_COMPUTATION : regroups some directories and files related to the simulation
        directories : CAS-MPI128-n with n= 5 to 50 (from simulation 5 to 50)
        each directory contains files checkcalc_00000.dat and checkdata_00000.dat
Come back to previous page