## 3D forward-facing step flow at $Re_H= 8304$ (turbulent inflow)
Database in progress … it is currently uncompleted

Author : Y. Fraigneau, LISN, UMR CNRS 9015 (yann.fraigneau@lisn.fr)
Date : August 2020
Simulation type : DNS (code Sunfluidh – Sunfluidh code)
Location : DATABASE_FORWARDFACINGSTEPFLOW2_RE8000_DNS
Status : Restricted access
Data size : ~ 8.6 Tb

A video is available here
Come back to first page

### Simulation settings

#### 2D sketch

#### Referential : cartesian geometry
1. axes :
  1. x(i) : downstream direction
  2. y(j) : normal direction
  3. z(k) : spanwise direction
2. origin :
  1. : the step
  2. : the bottom wall of the domain
  3. : the left side of the computational domain
#### Reference scales
- Density : mass density of the fluid ()
- Length : step height ()
- Velocity : inlet bulk velocity ()
- Dynamic viscosity : dynamic viscosity of the fluid ()
- Reynolds number :
#### Non-dimensionalised data
- velocity :
- density :
- coordinates : , ,
#### Computational domain
1. Domain scope
  1. Downstream direction(x) :
  2. Normal direction (y) :
  3. Spanwise direction (z) :
  4. Step position :
  5. Step height :
2. Boundary conditions
  1. Inlet : Turbulent boundary layer at , (boundary layer's thickness)
     , fluctuations generated from the SEM approach.
  2. Outlet : Orlansky's type at
  3. Wall conditions : Top and low walls of the domain
  4. Periodicity : lateral ends of the domain
3. Domain decomposition (200 MPI subdomains)
  1. Along the downstream direction :
    1. 15 (between the inlet and the outlet, above the step)
    2. 10 (between the inlet and the step)
  2. Along the normal direction : 4
  3. Along the spanwise direction : 4
  4. 2D sketch of domain decomposition in a plan {xy} (MPI process distribution (1))
     1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
     1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
     1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
     1 1 1 1 1 0 0 0 0 0 0 0 0 0 0
4. Spatial resolution
  1. Grid : per subdomain (471.859.200 cells over the domain)
  2. About cell-size
    1. (downstream direction)
    2. (normal direction)
    3. (spanwise direction)
Come back to first page

### Data features

- Time series from probes : U,V,W,P (velocity components & pressure)
  - Physical quantities : velocity components along x, y and z directions (u,v,w) and pressure (p)
  - 5 probes
  - Time step= 0.00945 time unit
  - Time range : from 120 to 700 time units
  - Locations (In vertical plan at )
    - Xi=-0.250 , Xj= 0.250 , Xk= 1.57 - MPI Subdomain ID :
    - Xi= 0.125 , Xj= 1.125 , Xk= 1.57 - MPI Subdomain ID :
    - Xi= 1.000 , Xj= 1.125 , Xk= 1.57 - MPI Subdomain ID :
    - Xi= 1.000 , Xj= 1.250 , Xk= 1.57 - MPI Subdomain ID :
    - Xi= 4.000 , Xj= 1.125 , Xk= 1.57 - MPI Subdomain ID :
File name (per physical quantity): x_ins_yyyyy.d with x= u,v,w,p and 'yyyyy' the MPI subdomain ID
- 3D snapshots
  - Instantaneous fields : velocity components in x, y and z directions (U,V,W) and pressure (P)
  - first dataset :
    - Recording rate : 0.5 time units
    - Time range from 120 to 729 time units
    - File name : res_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
      - MPI subdomain ID: from 0 to 199
      - Time ID : from 53 to 1270
- 2D slices
- Instantaneous fields : velocity components in x, y and z directions (U,V,W) and pressure (P)
- Recording rate : 0.1 time units
- Time range from 120 to 729 time units
- 4 slices are considered :
- slice 1 : normal direction z - position : z= 1.57 - MPI subdomains ID :
  - MPI subdomains ID : 1 to 197
- slices 4,5,6 : Wall pressure only
  - File name : slice_n_idir_xxxxx_yyyyyyy.d (n : slice number ID, idir : direction= 1: x(i), 2: y(j), 3: z(k), xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
  - slice 4 : normal direction y - position : y= 0.0 WARNING : available only from Time ID = 139 (corresponding to time > 386)
  - slice 5 : normal direction x - position : x= 0.0
  - slice 6 : normal direction y - position : y= 1.0
  - MPI subdomains ID : 4 to 7
  - MPI subdomains ID : 20 to 23
  - MPI subdomains ID : 36 to 39
  - MPI subdomains ID : 52 to 55
  - MPI subdomains ID : 68 to 71
  - MPI subdomains ID : 80 to 83
  - MPI subdomains ID : 92 to 95
  - MPI subdomains ID :104 to 107
  - MPI subdomains ID :116 to 119
  - MPI subdomains ID :128 to 131
  - MPI subdomains ID :140 to 143
  - MPI subdomains ID :152 to 155
  - MPI subdomains ID :164 to 167
  - MPI subdomains ID :176 to 179
  - MPI subdomains ID :188 to 191
  - Time ID : from 54 to 6363
- Statistics
  - fields : (i,j : indexes of direction x, y or z)
    - Mean fields of velocity components (<Ui>) and pressure (<P>)
    - Mean fields of quadratic quantities (<P2>, <UiUj>)
  - Time and space average computation (along the spanwise direction)
  - Time startup = 100.0 time units
  - Time range per file = 20.0 time units
  - Total time range from 100.0 to 720 time units
  - file name : rst_xxxxx_yyyyyyy.d (xxxxx : MPI subdomain ID, yyyyyyy : Time ID)
    - MPI subdomain ID : from 0 to 49 (MPI process rank where results about space average computation are stored)
    - Time ID : from 1 to 31
Come back to first page

### Database organisation

Data size : ~ 8.6 Tb
Main directory : /vol/DATABASE_MECA/RESTRICTED_ACCESS/DATABASE_FORWARDFACINGSTEPFLOW2_RE8000_DNS
For more details about files, see the the wiki doc of Sunfluidh
#### Directories & files
  /GRID : contains all ASCII files about grid setup
     input data file : data_meshgen.d
     report on grid features : report_meshgen.d
     grid files for sunfluidh: maillx.d, mailly.d, maillz.d
     check files (ASCII) : check_mesh_I.d,check_mesh_J.d,check_mesh_K.d
        (3 columns : indices, cell-face coordinates, cell size)
  /DATASETUP : ASCII files
   input data file for sunfluidh : input3d.dat
   data file for MPI subdomain distribution (MPI graphical topology): data_mpi_subdomain_layout.dat
  /TIMESERIES : contains time series recorded over the time range [120,680]
        ASCII files : x_ins_yyyyy.d with x= u,v,w,p
        time series files are sliced in storage directories CAS-MPI200-n (n from 53 to 255)
  /SNAPSHOTS : snapshots binary files res_xxxxx_yyyyyyy.d with a recording rate of 0.5 time unit
        files stored in archive files : res_yyyyyyy.tar for each time ID
  /STATISTICS : statistics binary files files rst_xxxxx_yyyyyyy.d
        files stored in archive files : res_z.tar , z is an ID number (from 1 to 31)
  /SLICES : slice binary files slice_n_idir_xxxxx_yyyyyyy.d
        files stored in archive files : slices_z.tar , z is an ID number (from 53 to 255)
  /RESTART_AR : backup/restart archive save_t145.tar and save_t45.tar at time=145 and 454 respectively
Come back to first page