## 2D flow around a heated square-cylinder - $Re_{h}= 50$, $Ra= 5\; 10^6$
A heated square-cylinder is placed in a channel flow

Author : Y. Fraigneau CNRS-LIMSI (yann.fraigneau@lisn.fr)
Date : June 2019
Simulation type : DNS (Sunfluidh code)
Location : /DATABASE_2DFLOW_AROUND_HEATED_SQUARECYLINDER_DNS
Status : Free access
Data size : ~ 3 Gb

A video is available here
Come back to first page

### Simulation settings

#### 2D sketch

#### Referential : cartesian geometry
1. axes :
  1. x(i) : downstream direction
  2. y(j) : normal direction
2. origin : lower left corner of the computational domain
#### Reference scales
- Density : mass density of the fluid ()
- Lengths : cylinder size () and the distance between the domain's top and the square-cylinder's top.
- Velocity : velocity at inlet ()
- Dynamic viscosity : dynamic viscosity of the fluid ()
- thermal diffusivity : ()
- Reynolds number :
- Rayleigh number :
#### Non-dimensionalised data
- velocity :
- density :
- coordinates : ,
- temperature : ( and are respectively the temperature imposed at the cylender's walls and the temperature at the inlet and channel's walls)
#### Computational domain
1. Domain scope
  1. computational domain size (channel flow)
    1. Downstream direction(x) : (upward part , downward part )
    2. Normal direction (y) :
  2. heated square cylinder
    1. size:
    2. wall temperature T_h^*= 1
1. Boundary conditions
  1. Inlet : imposed pressure uniform velocity ()
  2. Outlet : Orlansky type
  3. Bottom and top conditions : walls at (T_c^*=0)
2. Spatial resolution
  1. mesh size : (131.072 cells)
  2. About cell-size
    1. : from to (downstream direction)
    2. : from to (normal direction)
Come back to first page

### Data features

- Time series
  - Physical quantities : velocity components along x and y directions (u,v) and pressure (p)
  - 1 probe
  - Time step= time unit (irregular time step)
  - Time range : 250 time units
  - Location : Xi= 20.0 , Xj=2.0
  - File name (per physical quantity): x_ins_00000.d with x= u,v,t
- 3D snapshots
  - Instantaneous fields : velocity components in x, y and z directions (U,V), the pressure (P) and the phase function related to the body motion (TRACE)
  - Recording rate : 1 time unit
  - Time range from from 20.0 to 250.0 time units
  - File name : res_xxxxx_yyyyyyy.d
    - MPI subdomain ID: from 0 to 3 (case with MPI domain decomposition)
    - Time ID : from 0 to 250
Come back to first page

### Database organisation

Data size : ~ 3 Gb
Main directory : /vol/DATABASE_MECA/DATABASE_2DFLOW_HEATED_SQUARRECYLINDER_DNS
Directories & files

  /DATASETUP : ASCII files
        input data file for sunfluidh : input3d.dat (and input3d.dat_mpi4 for the case with MPI domain decomposition)
  /GRID : ASCII files
        input data file : data_meshgen.d
        grid files for sunfluidh: maillx.d, mailly.d, maillz.d (sequential case)
        mesh.tar (archive containing grid files for a domain decomposition with 4 MPI processes)
  /SNAPSHOTS : snapshots binary files res_xxxxx_yyyyyyy.d
  /SNAPSHOTS_MPI4 : snapshots resulting from a domain decomposition with 4 MPI processes
  /TIMESERIES : ASCII files
        u_ins_00000.d , v_ins_00000.d and t_ins_00000.d (timeseries of the velocity components and temperature from probe)
Come back to first page